## Slide 1
1
ARM CoreLink 400 & 500 Series System IP
PD Product Marketing December 2012

## Slide 2: ARM CoreLink™ and CoreSight™
System IP for the best ARM Cortex™ and Mali™ processor performance
Power efficient system
  Maximum cache & DDR utilization
  Shortest path to memory
System performance
  End-to-end QoS provides b/w & latency per master
Optimized system
  CoreSight debug and performance profiling
big.LITTLE™ test chip 2
System assured
  Designed together, verified together
CONFIDENTIAL

## Slide 3: CoreLink 400 System IP Available Now
Coherency
CoreLink CCI-400


Full cache coherency I/O coherency

CoreLink ADB-400
For DVFS
Virtualization
CoreLink MMU-400
OS level virtualization


CoreLink GIC-400


Virtual interrupts
Multi-processor support
External Memory Sub-system

CoreLink DMC-400


High DDR utilisation Integrated with DDR3 PHY

CoreLink TZC-400*
Secure regions
Rest of SoC Interconnect
CoreLink NIC-400


Low latency Routing efficiency
400 Series
cache
cache
cache
control
snoop
MMU
MMU
DVM mesaging
ADB-400
ADB-400
TZC-400
TZC-400
CONFIDENTIAL
* TZC-400 available 1Q13

## Slide 4: Wide Adoption of ARM System IP
CONFIDENTIAL
50,000 downloads of AMBA specs in last 3 years
80+ licensees of NIC-301, 12+ licensees of NIC-400
15+ licensees of CCI-400
10+ licensees of DMC-400
30 licensees of CoreSight SoC-400
Adopted across all market segments

## Slide 5: Updates to Existing CoreLink 400 Products
5
CoreLink NIC-400 smaller, faster, lower power


Hierarchical clock gating reduces idle power by 80% TLX-400 Thin Links to reduce routing
End-to-end QoS Virtual Networks across:
  CoreLink NIC-400 + QoS-400 + QVN-400
    Prevents blocking for higher multi master performance
  CoreLink CCI-400r1
    With enhanced throughput up to 25 GB/s @ 533MHz
  CoreLink DMC-400r1
    With integrated controller + PHY DDR3 28HPM
CoreLink TZC-400 secures regions in DRAM

## Slide 6: CoreLink CCI-400 Cache Coherent Interconnect
CONFIDENTIAL
6
First ARM interconnect to support AMBA 4 AXI Coherency Extensions (ACE)


Extends coherency to the system, multiple processors
Supports big.LITTLE™
Supports barriers, virtualisation, cache maintenance

Fixed 5x3 topology, configurable for performance/area from 100k to 500k gates
2x full ACE (CPU)
3x ACE-Lite + DVM I/O coherent slaves
3x master interfaces (2x DRAM + system)
End-to-end QoS with NIC-400 and DMC-400

Quad Cortex-A7
Coherent I/O device
Mali-T604 graphics
ADB-400
ADB-400
MMU-400
MMU-400
DMC-400
ACE
ACE-Lite
Other Slaves
Other Slaves
NIC-400
LCD
Video
Quad Cortex-A15
ACE
ACE
AXI4
AXI4
NIC-400
Configurable: AXI4/AXI3/AHB/APB
Configurable: AXI4/AXI3/AHB
DDR2/3 / LPDDR2
DDR2/3 / LPDDR2
ACE-Lite
ACE-Lite
PHY
PHY
GIC-400
ACE ACE-Lite + DVM ACE-Lite + DVM
CCI-400 Cache Coherent Interconnect 128-bit @ 0.5x CPU frequency
ACE-Lite ACE-Lite ACE-Lite
ACE-Lite + DVM
MMU-400

## Slide 7: CoreLink NIC-400 Network Interconnect
New in NIC-400:


20% faster, 20% smaller than NIC-301
Addition of AMBA 4 AXI4 interfaces and interconnect switches
Long burst support, QoS signalling
 + everything NIC-301 does, including support for AMBA 3 AXI, AHB, APB
Hierarchical clock gating
90% reduction in idle and near idle power on LP



Quality of Service Virtual Networks (QVN-400)



Separation of critical real-time traffic from high bandwidth low priority traffic Removes head of line and cross stream blocking
End-to-end QoS with CCI-400 and DMC-400

Advanced QoS Regulators (QoS-400)
New bandwidth sensitive dynamic regulator
Thin Links (TLX-400)
Packetized links between NIC-400s, masters & slaves, reduces routing, example 65% less wires at 2x freq, same bandwidth

Configurable Network Interconnect Structure

## Slide 8: CoreLink DMC-400 Dynamic Memory Controller
AMBA 4 Dynamic Memory Controller
Highly efficient interface from ARM systems to off chip LPDDR2 and DDR2 / DDR3 Delivers high bandwidth and low latency for high performance multimedia systems Effective management of power in memory sub-system





End-to-end QoS with NIC-400 and CCI-400
Improves performance for Cortex-A5, Cortex-A9, Cortex-R and Mali processor- based designs
Features and functionality



Configurable and programmable
Full support for advanced QoS-400 features
>90% max theoretical utilization of memory bus traffic


1, 2 or 4 system ports and memory channels Tight integration with ARM DDR3 PHY solutions

## Slide 9: CoreLink MMU-400 and GIC-400
I/O virtualization with distributed TLB maintenance messaging
Stage 2 address translation for hypervisor support
ARMv7 virtualization extension architecture compliant
Generic Interrupt Controller for multiple Cortex-A15, Cortex-A7 clusters
IRQs and FIQs securely managed by hypervisor for each OS
ARMv7 virtualization extension architecture compliant
GIC-400
MMU-400

## Slide 10: TZC-400 TrustZone Address Space Controller
CONFIDENTIAL
10
Extends secure memory with low cost external DRAM
Prevents illegal access to protected memory regions
Protection from software attacks
Part of TrustZone® system
Between CCI/NIC and DMC
Applications: secure transactions with sensitive data, DRM
Region 0
Region 1
Region 2
Master A
Address Map
Master B
Master C
Master D
Write
Read
Read
Read
Write
Write
Supports multiple interfaces (1, 2 or 4)
Secures 8 memory regions
Enables a secure data pipe
Setup read / write for specific masters
Fast Path for low latency masters
256 outstanding transactions
CoreLink™ CCI-400 Cache Coherent Interconnect
Cortex-A7
Coherent I/O device
128b
DMC-400
128b
ACE-Lite
ACE-Lite ACE-Lite
128b
Mali-T604
Graphics
ACE-Lite
Secure ROM
Secure RAM
ACE-Lite
128b
DMA-330 LCD
128b
ACE
AXI3
128b
AXI3
NIC-400
Configurable: AXI3/AHB-Lite/APB
AXI3/AHB
NIC-400
PHY
PHY
GIC-400
128b
ACE-Lite
ACE-Lite
ACE
128b
ACE
AXI3
TZC-400
ACE-Lite
128b
ACE-Lite
ACE-Lite
128b
ACE-Lite
DDR3/2 LPDDR2
DDR3/2 LPDDR2
TrustZone
Cortex- A15
ACE
TrustZone

## Slide 11: CoreSight SoC-400
A debug and trace framework for ARM based SoCs
Build the most effective on-chip visibility with CoreSight SoC IP
  Configurable debug & trace infrastructure to address all markets and latest processors
  SoC level time-stamping infrastructure
Improve productivity with CoreSight SoC flow
  Describe, check for compliance your CoreSight systems in minutes.
  Automated validation of your CoreSight systems
Unified flow for OEMs and silicon providers
  Based on IP-XACT 1.4 & AMBA Designer
A generic solution for all markets & processors


Integrate homogeneous & heterogeneous systems Trace Macrocells become add-ons

## Slide 12: CoreLink 400 Series for AMBA 3
NIC-400 configurable interconnect


High performance and rest of SoC interconnect AXI4, AXI3, AHB and APB4
Thin Links to reduce routing
  Between switches
End-to-end Quality of Service with virtual networks and regulation
  Separates low latency, real-time and high bandwidth masters
  Prevents head-of-line and cross-stream blocking
DMC-400 high efficiency, multi- channel memory controller


AXI3 and AXI4 supported Unified QoS mechanisms
MMU-400 assists hypervisor for I/O
  Stage 2 address translation
CoreLink NIC-400
Network Interconnect
MMU-400
DMC-400
AXI4
AXI3
AXI4
MALI GPU
AXI4
Other Slaves
Other Slaves
LCD
DMA-330
Dual Cortex-A
AXI3
AXI3
AXI3
X-bar switch
Configurable: AXI4/AXI3/AHB/APB
Configurable: AXI4/AXI3/AHB
NIC-400 switch
AXI4
DDR3/2 LPDDR2
ACE-Lite
PHY
AXI4
Thin Link
MMU-400
NIC-400 top level includes hierarchy of switches
X-bar switch
AXI4
Other Slaves
Other Slaves
AXI4
X-bar switch
Configurable: AXI4/AXI3/AHB/APB
Thin Link
L2C-310

## Slide 13: CoreLink 500 System IP for 2013
Support for ARMv8-A Cortex-A57 and Cortex-A53 SoCs
CoreLink CCN-504 Cache Coherent Network
  Up to 4 clusters of Cortex-A57, Cortex-A53 and Cortex-A15
  ~1 terabit/sec useable system bandwidth
CoreLink DMC-520 Dynamic Memory Controller
  72-bit DDR4-3200 and interfaces directly with CCN-504
CoreLink GIC-500 Generic Interrupt Controller
  GICv3 Architecture for interrupt scaling with affinity routing
  Message based interrupts and direct GICCPU interface
CoreLink MMU-500 System Memory Management Unit
  2 stages of address translation
  System MMU Architecture v2 with new 64k page tables
  Up to 48-bit addressing for IO device virtualization

## Slide 14: Example High End Mobile Solution
CCI-400
Mali GPU
ADB-400
ADB-400
Quad
Cortex-A53
ACE
ACE
ACE-Lite
ACE-Lite
ACE-Lite
ACE-Lite
ACE-Lite
Other Slaves
Other Slaves
IPU
DMA-330
Dual Cortex- A57
ACE
ACE
AXI4
AXI4
NIC-400
Configurable: AXI4/AXI3/AHB/APB
GIC-500
ACE-Lite
ACE-Lite + DVM
MMU-500
ADB-400
ADB-400
DMC-400
DDR3/2 LPDDR2
ACE-Lite
ACE-Lite
PHY
PHY
DDR3/2 LPDDR2
ACE-Lite
Cortex- M3
AHB
AXI3
NIC-400
TZC-400
TZC-400
Cortex
-R7
Cortex
-R7
TZC-400
TZC-400
DSP
AXI3
NIC-400
AXI3
AXI3
AXI3
AXI3
AXI3
Thin Link
Thin Link
AXI4
System Control Processor
AXI3
AXI3
NIC-400
AXI3
LCD
Ctrl
Video Ctrl

## Slide 15: Growing Importance of Virtualization
App 1
Operating System
Hardware
Virtualization hardware supported in ARMv7-A, ARMv8-A “Virtualization is execution of software in an environment separated from the underlying hardware resources”
Virtualization use cases
IP obfuscation; IP protection; environment duplication; multiple guest-OS support under hypervisor control
System without virtualization System with virtualization
App 2
App 1
App 2
Guest OS 1
App 1
App 2
Guest OS 2
Virtual Machine Monitor (VMM, or Hypervisor)
Hardware
Virtual Machine 1
Virtual Machine 2

## Slide 16: Virtualization with MMU-500
CCI-400
ACE-Lite
NIC-400
Flash
GPIO
DSP
Cortex-A15
ACE
AXI4
Configurable: AXI4/AXI3/AHB/APB
GIC-400
ACE-Lite
AXI3
Cortex-A7
ACE
ACE
ACE
LPDDR2
Audio
GPU
Cortex-M3
ACE-Lite
AHB
NIC-400
AXI4
TBU
MMU-500
TBU
DVM ACE-Lite
ACE-Lite
ACE-Lite
DMC-400
PHY
Nested translation
  Stage 1 and Stage 2
  Supports virtual address (VA) programming of devices
  Scatter/gather function
Adds ARMv8 support
  To enable interoperability with Cortex-A57 & Cortex-A53
  Also supports Cortex-A15 and Cortex-A7 page table formats
TBUMMUT-C5U 00

## Slide 17: Virtualization with MMU-500
CCI-400
ACE-Lite
NIC-400
Flash
GPIO
DSP
Cortex-A15
ACE
AXI4
Configurable: AXI4/AXI3/AHB/APB
GIC-400
ACE-Lite
ACE-Lite
AXI3
Cortex-A7
ACE
ACE
ACE
LPDDR2
Audio
GPU
Cortex-M3
ACE-Lite
AHB
NIC-400
AXI4
TBU
TBU
TCU
MMU-500
TBU
DVM
ACE-Lite
ACE-Lite
DMC-400
PHY
ARM System MMU Terminology:
TBU =
TCU =
Translation Buffer Unit (containing the TLB)
Translation Control Unit (containing the page table walker)
Nested translation
  Stage 1 and Stage 2
  Supports virtual address (VA) programming of devices
  Scatter/gather function
Adds ARMv8 support
  To enable interoperability with Cortex-A57 & Cortex-A53
  Also supports Cortex-A15 and Cortex-A7 page table formats
Distributed TLBs
  To increase TLB efficiency and to save power and area
  Point-to-point connection
  n x 1:1 TLBTCU interfaces

## Slide 18: Generic Interrupt Controller for ARMv8
GIC-500 supports 48 CPUs
Cortex-A57 and Cortex-A53
GICv3 architecture
Shared Peripheral Interrupts
Up to 960 SPIs
Direct to AL0 or all
Message based interrupts
Lower cost per interrupt
Direct to AL0
MSI(-X) support
VMs can directly program peripherals to reduce hypervisor overhead
Affinity level routing
Allows for scalability
Consolidated as one monolithic block for GIC-500
SPI = Shared Peripheral Interrupt (wired interrupt)
LPI = Local Peripheral Interrupt (message based interrupt)
SPIs
CPU I/F
0
CPU I/F
1
2
CPU I/F CPU I/F
3
CPU I/F
0
CPU I/F
1
CPU I/F CPU I/F
2 3
CPU I/F
0
CPU I/F
1
CPU I/F CPU I/F
2 3
CPU I/F
0
CPU I/F
1
2
CPU I/F CPU I/F
3
0
1
2
n
CoreLink GIC-500
CPU 0.0.1.2
Interrupt Re-distribution –
Logical View
CPU *
0
Affinity 0
Affinity 1 0
Affinity 2
Affinity 3
LPIs
CPU 0.0.1.2

## Slide 19: High Performance, Efficient, Cache Coherent
NIC-400 Network Interconnect
Flash GPIO
NIC-400
USB
Quad Cortex-A57
L2 cache
GIC-500
CoreLink™ DMC-520
x72 DDR4-3200
Snoop Filter
Quad Cortex-A57
L2 cache
Quad Cortex-A57
L2 cache
Quad Cortex-A57
L2 cache
CoreLink™ DMC-520
x72 DDR4-3200
PCIe
10-40
GbE
DPI
Crypto
CoreLink™ CCN-504 Cache Coherent Network
8/16MB L3 cache
MMU-500
DSP
DSP
DSP
SATA
Dual channel DDR3/4 x72
Up to 4 cores per cluster
4 fully coherent clusters
Integrated L3 cache
18 AMBA ACE-Lite
interfaces for I/O coherency
Peripheral address space
Heterogeneous processors – CPU, GPU, DSP and accelerators
128-bit bus @ CPU
frequency
To minimize snoop traffic
Usable system bandwidth: ~ 1 Terabit/second

## Slide 20: Scalable System Features
CoreLink CCN-504 | 
CPU | 4 ports up to 16 cores Cortex-A57, Cortex- A53 and Cortex-A15
IO | 18 ports: AMBA® 4 AXI4/ACE-Lite interfaces
DDR | 2 channels supported with CoreLink DMC- 520
RAS | ECC on RAMs and parity on transport
QoS | QoS regulation and priority management
Security | TrustZone aware
Low Power Support | Extensive clock gating, leakage mitigation hooks, Granular DVFS and CPU shutdown support, Partial or full L3 cache shutdown, Retention modes

## Slide 21: Security, Reliability, Quality of Service
5th Generation ARM DMC targeting >95% DRAM efficiency
  ECC and RAS features
  Performance Profiling
  TrustZone Address Space Control
High efficiency through close integration with CCN-504
  System wide QoS, designed and verified with ARM CPUs
RAS = Reliability, Availability, Serviceability
Artisan® DDR4, 3 & 3L PHY 3200 Mbps
CoreLink DMC-520

## Slide 22: High Performance Memory Access
CoreLink DMC-520 | 
Performance | Max bandwidth: 25.6 GB/s per channel Buffering to optimize read/write turnaround
Interfaces | Optimal direct connection to CCN-504 Industry standard DFI-3.0 to connect to PHY
PHY | Low-latency PHY from ARM
Memory | Support for x72 DRAM DDR3, DDR3L and DDR4 up to DDR4-3200
Low Power Support | Programmable DRAM power modes

## Slide 23: CoreLink End-to-End QoS Architecture
Enterprise Requirements
“Bursty” datapath


High peak bandwidth Multiple interfaces









CoreLink End-to-End QoS
QoS field for every transaction Fixed, programmable or regulated End-to-End propagation
Programmable QoS mechanisms Regulation of all traffic on ingress Bandwidth management
Latency management
QoS re-ordering and arbitration
Interconnect ingress Non-blocking transport L3 cache
DMC
CPU
Accel
IO
L3
DDR
“Compute intensive” Control Path
  Lowest latency requirements
“Latency Sensitive” Air interface
  Predictable Latency

## Slide 24: CoreSight SoC-400 for ARMv8
EETTMM
Quad
Mali
GPU
Cortex-A53
ACE
ACE-Lite
NIC-400
Other Slaves
Other Slaves
IPU
DMA-330
Dual
Cortex-
A57
ACE
ACE
AXI4
AXI4
GIC-500
ADB-400
DMC-400
DDR3/2 LPDDR2
ACE-Lite
ACE-Lite
PHY
PHY
DDR3/2 LPDDR2
ACE-Lite
C
ortex-
M3
AHB
AXI3
NIC-400
TZC-400
NIC-400
Cortex
-R7
Cortex
-R7
TZC-400
TZC-400
DSP
AXI3
AXI3
AXI3
AXI3
AXI3
AXI3
Thin Link
Thin Link
AXI4
System Control Processor
AXI3
AXI3
NIC-400
AXI3
LCD
Ctrl
Video Ctrl
ETM
ETM
EETTMM
STM
Trace bus
TPIU
Debug bus
DAP
SWD/ JTAG
ADBB-40o0 thAADB-R400 MvAD7B-4&00 ARMMMUv-5080
processors
aArCEe sAuCEp-LiteportAeCE-dLite bAyCE-LiCte + DoVMreSight SoC-400
Support foCCrI-4C00ortex-A53 & Cortex-A57
ACE-Laite vailable frACoE-Lmite
core’sACLE-LAite C release
TZC-400

Embedded Trace Macrocells (ETM)
provided with processCoonfigrurasble: AXI4/AXI3/AHB/APB

## Slide 25: Summary
CoreLink 400 series is available now
  Coherency support for Cortex-A15, Cortex-A7 and the latest Cortex-A50 series
  NIC-400 Network Interconnect for Cortex-A and Cortex-R series processors
CoreLink 500 series offers new system scaling
  16 core support in CCN-504 Cache Coherent Network for enterprise applications
  Enterprise DDR3/4 memory support with DMC-520
  ARMv8 page stable support with MMU-500
ARM CoreLink System IP offers the best ARM Cortex and Mali™ processor performance
  Designed together, validated together